## Slide 1
S0
reset
S1
start
S3
sensor ID
‘[’
Parse Data Request
S1-S3 have a timeout not listed on diagram to return to S0
S0: ready state, wait for input
S1: received start byte, wait for module ID
S2: received module ID, wait for sensor ID, check module ID validity
S3: received sensor ID, wait for checksum
S4: received checksum, wait for end byte, verify checksum
0-9
char
‘]’
incorrect ID
S4
checksum
0-9
S2
module ID

## Slide 2
S6
exec
S1
start
S2
module ID
S3
sensor ID
S5
checksum
0-9
S4
data
S0
reset
char[0..n]
Data Receive on
Master Module
S1-S4 have a timeout not listed on diagram to return to S0
S0: ready state, wait for input
S1: received start byte, wait for module ID
S2: received module ID, wait for sensor ID
S3: received sensor ID, calculate expected data bytes, wait for data bytes
S4: loop through n times where n is number of data bytes expected plus the checksum
S5: received end byte, calculate checksum and compare to validate transmission
S6: send data to Ground Station, translate data from char to proper format (integer, double), save numeric data to SD card
A-Z
Char[0..n]
0-9
bad module ID
data[n+1]
‘]’
bad checksum